143A: Principles of Operating Systems
Lecture 6: Address translation
Anton Burtsev
January, 2017

---
Address translation

---
Segmentation

---
Descriptor table

---
Descriptor table

---
Segment descriptors
- Base address
  - 0 – 4 GB
- Limit (size)
  - 0 – 4 GB
- Access rights
  - Executable, readable, writable
  - Privilege level (0 - 3)

---
Segment descriptors

---
Segment registers
- Hold 16 bit segment selectors
  - Pointers into a special table
  - Global or local descriptor table
- Segments are associated with one of three types of storage
  - Code
  - Data
  - Stack

---
Code segment
- Code
  - CS register
  - EIP is an offset inside the segment stored in CS
- Can only be changed with
  - procedure calls,
  - interrupt handling, or
  - task switching

---
Data segment
- Data
  - DS, ES, FS, GS
  - 4 possible data segments can be used at the same time

---
Stack segment
- Stack
  - SS
- Can be loaded explicitly
  - OS can set up multiple stacks
  - Of course, only one is accessible at a time

---
Programming model
- Segments for: code, data, stack, “extra”
  - A program can have up to 6 total segments
  - Segments identified by registers: cs, ds, ss, es, fs, gs
- Prefix all memory accesses with desired segment:
  - mov eax, ds:0x80 (load offset 0x80 from data into eax)
  - jmp cs:0xab8 (jump execution to code offset 0xab8)
  - mov ss:0x40, ecx (move ecx to stack offset 0x40)

---
Segmented programming (not real)
static int x = 1;
int y; // stack
if (x) {
    y = 1;
    printf (“Boo”);
} else
    y = 0;
ds:x = 1; // data
ss:y; // stack
if (ds:x) {
   ss:y = 1;
   cs:printf(ds:“Boo”);
} else
   ss:y = 0;

---
Programming model, cont.
- This is cumbersome, so infer code, data and stack segments by instruction type:
  - Control-flow instructions use code segment (jump, call)
  - Stack management (push/pop) uses stack
  - Most loads/stores use data segment
- Extra segments (es, fs, gs) must be used explicitly

---
Logical address
Segment selector (16 bit) + offset (32 bit)

---
Paging

---
Paging idea
- Break up memory into 4096-byte chunks called pages
  - Modern hardware supports 2MB, 4MB, and 1GB pages
- Independently control mapping for each page of linear address space
- Compare with segmentation (single base + limit)
  - many more degrees of freedom

---
Why do we need paging?
- Illusion of a private address space
  - Identical copy of an address space in multiple programs
    - Remember fork()?
  - Simplifies software architecture
    - One program is not restricted by the memory layout of the others

---
Why do we need paging?
- Illusion of a private address space
  - Identical copy of an address space in multiple programs
    - Remember fork()?
  - Simplifies software architecture
    - One program is not restricted by the memory layout of the others
- Emulate large virtual address space on a smaller physical memory
  - Swap rarely accessed pages to disk

---
Why do we need paging?
- Share a region of memory across multiple programs
  - Communication (shared buffer of messages)
  - Shared libraries
- Isolate parts of the program
- Isolate programs from OS

---
Page translation

---
Page translation

---
Page directory entry (PDE)
- 20 bit address of the page table
  - Pages 4KB each, we need 1M to cover 4GB
- R/W – writes allowed?
  - To a 4MB region controlled by this entry
- U/S – user/supervisor
  - If 0 – user-mode access is not allowed
- A – accessed

---
Page table entry (PTE)
- 20 bit address of the 4KB page
  - Pages 4KB each, we need 1M to cover 4GB
- R/W – writes allowed?
  - To a 4KB page
- U/S – user/supervisor
  - If 0 user-mode access is not allowed
- A – accessed
- D – dirty – software has written to this page

---
Page translation

---
Back of the envelope
- If a page is 4K and an entry is 4 bytes, how many entries per page?
  - 1k
- How large of an address space can 1 page represent?
  - 1k entries * 1page/entry * 4K/page = 4MB
- How large can we get with a second level of translation?
  - 1k tables/dir * 1k entries/table * 4k/page = 4 GB
  - Nice that it works out that way!

---
Questions?

---
References

---
TLB
- CPU caches results of page table walks
  - In translation lookaside buffer (TLB)
- Walking page table is slow
  - Each memory access is 200-300 cycles on modern hardware
  - L3 cache access is 70 cycles
Virt	Phys
0xf0231000	0x1000
0x00b31000	0x1f000
0xb0002000	0xc1000
-	-
cr3

---
TLB
- TLB is a cache (in CPU)
  - It is not coherent with memory
  - If page table entry is changes, TLB remains the same and is out of sync
cr3
Virt	Phys
0xf0231000	0x1000
0x00b31000	0x1f000
0xb0002000	0xc1000
-	-
Same
Virt Addr.
No Change!!!

---
Invalidating TLB
- After every page table update, OS needs to manually invalidate cached values
- Modern CPUs have “tagged TLBs”,
  - Each TLB entry has a “tag” – identifier of a process
  - No need to flush TLBs on context switch
- On Intel this mechanism is called
  - Process-Context Identifiers (PCIDs)

---
More paging tricks
Determine a working set of a program?

---
More paging tricks
- Determine a working set of a program?
  - Use “accessed” bit

---
More paging tricks
- Determine a working set of a program?
  - Use “accessed” bit
- Iterative copy of a working set?
  - Used for virtual machine migration

---
More paging tricks
- Determine a working set of a program?
  - Use “accessed” bit
- Iterative copy of a working set?
  - Used for virtual machine migration
  - Use “dirty” bit

---
More paging tricks
- Determine a working set of a program?
  - Use “accessed” bit
- Iterative copy of a working set?
  - Used for virtual machine migration
  - Use “dirty” bit
- Copy-on-write memory, e.g. lightweigh fork()?

---
More paging tricks
- Determine a working set of a program?
  - Use “accessed” bit
- Iterative copy of a working set?
  - Used for virtual machine migration
  - Use “dirty” bit
- Copy-on-write memory, e.g. lightweight fork()?
  - Map page as read/only

---
When would you disable paging?

---
When would you disable paging?
- Imagine you're running a memcached
  - Key/value cache
- You serve 1024 byte values (typical) on 10Gbps connection
  - 1024 byte packets can leave every 835ns, or 1670 cycles (2GHz machine)
  - This is your target budget per packet

---
When would you disable paging?
- Now, to cover 32GB RAM with 4K pages
  - You need 64MB space
  - 64bit architecture, 3-level page tables
- Page tables do not fit in L3 cache
  - Modern servers come with 32MB cache
- Every cache miss results in up to 3 cache misses due to page walk (remember 3-level page tables)
  - Each cache miss is 200 cycles
- Solution: 1GB pages

---
Page translation for 4MB pages