143A: Principles of Operating Systems
Lecture 09: First process
Anton Burtsev
January, 2017

---
Recap: Can a process overwrite kernel memory?

---
Privilege levels
- Each segment has a privilege level
  - DPL (descriptor privilege level)
  - 4 privilege levels ranging 0-3

---
Privilege levels
- Currently running code also has privilege level
  - “Current privilege level” (CPL): 0-3
  - Can access only less privileged segments
    - E.g., 0 can access 1, 2, 3
- Some instructions are “privileged”
  - Can only be invoked at CPL = 0
  - Examples:
    - Load GDT
    - MOV <control register>
      - E.g. reload a page table by changing CR3

---
Real world
- Only two privilege levels are used in modern OSes:
  - OS kernel runs at 0
  - User code runs at 3
- This is called “flat” segment model
  - Segments for both 0 and 3 cover entire address space
- But then... how the kernel is protected?
  - Page tables

---
Page table: user bit
- Each entry (both Level 1 and Level 2) has a bit
  - If set, code at privilege level 3 can access
  - If not, only levels 0-2 can access
- Note, only 2 levels, not 4 like with segments
- All kernel code is mapped with the user bit clear
  - This protects user-level code from accessing the kernel

---
TLB
- CPU caches results of page table walks
  - In translation lookaside buffer (TLB)
- Walking page table is slow
  - Each memory access is 200-300 cycles on modern hardware
  - L3 cache access is 70 cycles
Virt	Phys
0xf0231000	0x1000
0x00b31000	0x1f000
0xb0002000	0xc1000
-	-
cr3

---
TLB
- TLB is a cache (in CPU)
  - It is not coherent with memory
  - If page table entry is changes, TLB remains the same and is out of sync
cr3
Virt	Phys
0xf0231000	0x1000
0x00b31000	0x1f000
0xb0002000	0xc1000
-	-
Same
Virt Addr.
No Change!!!

---
Invalidating TLB
- After every page table update, OS needs to manually invalidate cached values
- Modern CPUs have “tagged TLBs”,
  - Each TLB entry has a “tag” – identifier of a process
  - No need to flush TLBs on context switch
- On Intel this mechanism is called
  - Process-Context Identifiers (PCIDs)

---
Creating Processes

---
Recap: kernel memory layout

---
Process memory layout

---
How does kernel creates new processes?

---
How does kernel creates new processes?
- Exec
  - exec(“/bin/ls”, argv);

---
exec(): high-level outline
- We want to create the following layout
- What shall we do?

---
exec(): high-level outline
- Load program from disk
- Create user-stack
- Run!

---
exec(): locate inode
6309 int
6310 exec(char *path, char **argv)
6311 {
...
6321 if((ip = namei(path)) == 0){
6322 end_op();
6323 return −1;
6324 }
6328 // Check ELF header
6329 if(readi(ip, (char*)&elf, 0, sizeof(elf)) <
        sizeof(elf))
6330 goto bad;
6331 if(elf.magic != ELF_MAGIC)
6332 goto bad;

---
exec(): check ELF header
6309 int
6310 exec(char *path, char **argv)
6311 {
...
6321 if((ip = namei(path)) == 0){
6322 end_op();
6323 return −1;
6324 }
6328 // Check ELF header
6329 if(readi(ip, (char*)&elf, 0, sizeof(elf)) <
        sizeof(elf))
6330 goto bad;
6331 if(elf.magic != ELF_MAGIC)
6332 goto bad;

---
Setup kernel address space()
6333
6334 if((pgdir = setupkvm()) == 0)
6335 goto bad;
6336

---
Remember: each process maps kernel in its page table

---
allocuvm(): allocate user pages

---
loaduvm(): read program from disk

---
exec(): allocate process' stack
- Allocate two pages
  - One will be stack
  - Mark another one as inaccessible
6361 sz = PGROUNDUP(sz);
6362 if((sz = allocuvm(pgdir, sz, sz + 2*PGSIZE)) == 0)
6363 goto bad;
6364 clearpteu(pgdir, (char*)(sz − 2*PGSIZE));
6365 sp = sz;

---
Allocate stack

---
Switch page tables
- Switch page tables
- Deallocate old page table
6398 switchuvm(proc);
6399 freevm(oldpgdir);
6400 return 0;

---
Wait... which page table we are deallocating?

---
Wait... which page table we are deallocating?
- Remember exec() replaces content of an already existing process
  - That process had a page table
  - We have to deallocate it

---
Deallocate address space

---
Outline: deallocate process address space
- Walk the page table
  - Deallocate all pages mapped by the page table
- Deallocate pages that contain Level 2 of the page-table
- Deallocate page directory

---
2015 freevm(pde_t *pgdir)
2016 {
2017 uint i;
2018
2019 if(pgdir == 0)
2020 panic("freevm: no pgdir");
2021 deallocuvm(pgdir, KERNBASE, 0);
2022 for(i = 0; i < NPDENTRIES; i++){
2023 if(pgdir[i] & PTE_P){
2024 char * v = P2V(PTE_ADDR(pgdir[i]));
2025 kfree(v);
2026 }
2027 }
2028 kfree((char*)pgdir);
2029 }
Deallocate user address space

---
1987 deallocuvm(pde_t *pgdir, uint oldsz, uint newsz)
1988 {
...
1995 a = PGROUNDUP(newsz);
1996 for(; a < oldsz; a += PGSIZE){
1997 pte = walkpgdir(pgdir, (char*)a, 0);
1998 if(!pte)
1999 a += (NPTENTRIES − 1) * PGSIZE;
2000 else if((*pte & PTE_P) != 0){
2001 pa = PTE_ADDR(*pte);
2002 if(pa == 0)
2003 panic("kfree");
2004 char *v = P2V(pa);
2005 kfree(v);
2006 *pte = 0;
2007 }
2008 }
2009 return newsz;
2010 }
Walk page table and get pte

---
1987 deallocuvm(pde_t *pgdir, uint oldsz, uint newsz)
1988 {
...
1995 a = PGROUNDUP(newsz);
1996 for(; a < oldsz; a += PGSIZE){
1997 pte = walkpgdir(pgdir, (char*)a, 0);
1998 if(!pte)
1999 a += (NPTENTRIES − 1) * PGSIZE;
2000 else if((*pte & PTE_P) != 0){
2001 pa = PTE_ADDR(*pte);
2002 if(pa == 0)
2003 panic("kfree");
2004 char *v = P2V(pa);
2005 kfree(v);
2006 *pte = 0;
2007 }
2008 }
2009 return newsz;
2010 }
Deallocate a page

---
Deallocate Level 2
2015 freevm(pde_t *pgdir)
2016 {
2017 uint i;
2018
2019 if(pgdir == 0)
2020 panic("freevm: no pgdir");
2021 deallocuvm(pgdir, KERNBASE, 0);
2022 for(i = 0; i < NPDENTRIES; i++){
2023 if(pgdir[i] & PTE_P){
2024 char * v = P2V(PTE_ADDR(pgdir[i]));
2025 kfree(v);
2026 }
2027 }
2028 kfree((char*)pgdir);
2029 }

---
Recap
- We know how exec works!
- We can create new processes

---
Questions?