ICS143A: Principles of Operating Systems
Lecture 12: Interrupts and Exceptions
Anton Burtsev
October, 2017

---
Why do we need interrupts?
 Remember:
hardware interface is designed to help OS

---
Why do we need interrupts?
- Fix an abnormal condition
  - Page not mapped in memory
- Notifications from external devices
  - Network packet received
- Preemptive scheduling
  - Timer interrupt
- Secure interface between OS and applications
  - System calls

---
Two types:
synchronous and asynchronous

---
Synchronous
- Exceptions – react to an abnormal condition
  - E.g., page mapping (virtual address) is not present in the page table
    - Bring the swapped page back to memory (copy from disk)
    - Fix the page-table entry
  - Invoke a system call
    - Transition from user-level to kernel (more later)
  - Intel distinguishes 3 types: faults, traps, aborts
Asynchronous
- Interrupts – preempt normal execution
  - Notify that something has happened
    - New packet from the network, disk I/O completed, timer tick, notification from another CPU)

---
Handling interrupts and exceptions
- Same procedure
  - Stop execution of the current program
  - Start execution of a handler
  - Processor accesses the handler through an entry in the Interrupt Descriptor Table (IDT)
- Each interrupt is defined by a number
  - E.g., 14 is pagefault, 3 debug
  - This number is an index into the interrupt table (IDT)

---
Interrupt path
no change in privilege level
e.g., we're already running in the kernel

---
CPU
CPU
Memory

---
Interrupt descriptor

---
Interrupt descriptor

---
Interrupt handlers
- Just plain old code in the kernel
- The IDT stores a pointer to the right handler routine

---
Interrupt path

---
Processing of interrupt (same PL)
1. Push the current contents of the EFLAGS, CS, and EIP registers (in that order) on the stack
2. Push an error code (if appropriate) on the stack
3. Load the segment selector for the new code segment and the new instruction pointer (from the interrupt gate or trap gate) into the CS and EIP registers
4. If the call is through an interrupt gate, clear the IF flag in the EFLAGS register (disable further interrupts)
5. Begin execution of the handler

---
Interrupt path

---
Processing of interrupt (cross PL)
Need to change privilege level...

---
Detour:
What are those privilege levels?

---
Recap: Can a process overwrite kernel memory?

---
Privilege levels
- Each segment has a privilege level
  - DPL (descriptor privilege level)
  - 4 privilege levels ranging 0-3

---
Privilege levels
- Currently running code also has a privilege level
  - “Current privilege level” (CPL): 0-3
  - It is saved in the %cs register

---
WAT!

---
Segmented programming (not real)
static int x = 1;
int y; // stack
if (x) {
    y = 1;
    printf (“Boo”);
} else
    y = 0;
ds:x = 1; // data
ss:y; // stack
if (ds:x) {
   ss:y = 1;
   cs:printf(ds:“Boo”);
} else
   ss:y = 0;

---
Actual switch
Use long jump to change code segment
9153 ljmp $(SEG_KCODE<<3), $start32
  - Explicitly specify code segment, and address
  - Segment is 0b1000 (0x8)

---
Privilege level transitions
- CPL can access only less privileged segments
    - E.g., 0 can access 1, 2, 3
- Some instructions are “privileged”
  - Can only be invoked at CPL = 0
  - Examples:
    - Load GDT
    - MOV <control register>
      - E.g. reload a page table by changing CR3

---
Real world
- Only two privilege levels are used in modern OSes:
  - OS kernel runs at 0
  - User code runs at 3
- This is called “flat” segment model
  - Segments for both 0 and 3 cover entire address space
- But then... how the kernel is protected?
  - Page tables

---
Page table: user bit
- Each entry (both Level 1 and Level 2) has a bit
  - If set, code at privilege level 3 can access
  - If not, only levels 0-2 can access
- Note, only 2 levels, not 4 like with segments
- All kernel code is mapped with the user bit clear
  - This protects user-level code from accessing the kernel

---
End of detour:
Back to handling interrupts

---
Thank you.